GestureID		@ 0x01
	Bit7	Bit6	Bit5	Bit4		Bit3	Bit2	Bit1	Bit0
Desc.				GestureID
	Bit Name			description
	[7: 0] GestureID			Gesture code
				0x00: no gesture
				0x01: on a slippery / 0x02: decline
				0x03: Left slip
				0x04: Right slide / 0x05: Click
				0x0B: Double-click
				0x0C: Press

FingerNum		@ 0x02
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
Desc.				FingerNum
	Bit Name			description
	[7: 0] FingerNum			The number of fingers. / 0: No / 1 finger: a finger
XposH		@ 0x03
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
Desc.						Xpos [11: 8]
	Bit Name			description
	[3: 0] XPos			X coordinate of the upper 4 bits
XposL		@ 0x04
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
Desc.				Xpos [7: 0]
	Bit Name			description
	[7: 0] XPos			X coordinate of the lower 8 bits
YposH		@ 0x05
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
Desc.						Ypos [11: 8]
	Bit Name			description
	[3: 0] YPos			Y coordinate of the upper 4 bits
YposL		@ 0x06
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
Desc.				Ypos [7: 0]
	Bit Name			description
	[7: 0] YPos			Y coordinate of the lower 8 bits
BPC0H		@ 0xB0
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
Desc.				BPC0 [15: 8]

	Bit Name			description
	[7: 0] BPC0H			BPC0 value of upper 8 bits
BPC0L		@ 0xB1
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.				BPC0 [7: 0]
	Bit Name			description
	[7: 0] BPC0L			The lower 8 bits of the value BPC0
BPC1H		@ 0xB2
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.				BPC1 [15: 8]
	Bit Name			description
	[7: 0] BPC1H			BPC1 high value 8
BPC1L		@ 0xB3
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.				BPC1 [7: 0]
	Bit Name			description
	[7: 0] BPC1L			The lower 8 bits of the value BPC1
ChipID		@ 0xA7
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.				ChipID
	Bit Name			description
	[7: 0] ChipID			DH
ProjID		@ 0xA8
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.				ProjID
	Bit Name			description
	[7: 0] ProjID			Project Number
FwVersion		@ 0xA9
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.				FwVersion
	Bit Name			description
	[7: 0] FwVersion			Software version number
MotionMask		@ 0xEC
	Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1	Bit0
Desc.							EnConLR EnConUD EnDClick
	Bit Name			description
[2]		EnConLR		Continuous operation can slide around
[1]		EnConUD		Slide up and down to enable continuous operation
[0]		EnDClick		Enable Double-click action

IrqPluseWidth		@ 0xED
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				IrqPluseWidth
	Bit Name			description
	[7: 0] IrqPluseWidth			Interrupt output low pulse width.
				Unit 0.1ms, optional values: 1-200. The default value is 10.
NorScanPer		@ 0xEE
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				NorScanPer
	Bit Name			description
	[7: 0] NorScanPer			Rapid detection of the normal cycle.
				This value will affect the LpAutoWakeTime and AutoSleepTime. Units of 10ms,
				selectable values: 1 to 30. The default is 1.
MotionSlAngle		@ 0xEF
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				MotionSlAngle
	Bit Name			description
	[7: 0] MotionSlAngle			Sliding partition gesture detection angle control. Angle = tan (c) * 10 c is a
				positive x-axis direction as a reference angle.
LpScanRaw1H		@ 0xF0
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				LpScanRaw1H
	Bit Name			description
	[7: 0] LpScanRaw1H			Scanning the reference channel 1 low power 8-bit value is high.
LpScanRaw1L		@ 0xF1
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				LpScanRaw1L
	Bit Name			description
	[7: 0] LpScanRaw1L			The lower 8 bits of the reference value of the low-power scanning No. 1 channel.
LpScanRaw2H		@ 0xF2
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				LpScanRaw2H
	Bit Name			description
	[7: 0] LpScanRaw2H			Scanning the reference channel 1 low power 8-bit value is high.
LpScanRaw2L		@ 0xF3
	Bit7	Bit6	Bit5	Bit4	Bit3		Bit2	Bit1	Bit0
Desc.				LpScanRaw2L
	Bit Name			description
	[7: 0] LpScanRaw2L			The lower 8 bits of the reference value of the low-power scanning No. 1 channel.
LpAutoWakeTime		@ 0xF4

Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0

Desc.	LpAutoWakeTime

Bit Name	description

[7: 0] Auto-calibration cycle LpAutoWakeTime low power consumption.

Unit 1 minute optional value: 1-5. The default is 5.

LpScanTH			@ 0xF5
		Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1		Bit0
Desc.					LpScanTH
		Bit Name			description
		[7: 0] LpScanTH			Low-power scanning wake threshold. The smaller the more
					sensitive. Optional Value: 1 to 255. The default value is 48.
LpScanWin			@ 0xF6
		Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1		Bit0
Desc.					LpScanWin
		Bit Name			description
		[7: 0] LpScanWin			Low-power scanning range. The greater the sensitivity, the higher the
					power consumption. Optional value: 0,1,2,3. The default is 3.
LpScanFreq			@ 0xF7
		Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1		Bit0
Desc.					LpScanFreq
		Bit Name			description
		[7: 0] LpScanFreq			Low-power scanning frequency. The smaller the
					more sensitive. Optional Value: 1 to 255. The default value is 7.
LpScanIdac			@ 0xF8
		Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1		Bit0
Desc.					LpScanIdac
		Bit Name			description
		[7: 0] LpScanIdac			Low power scan current. The smaller the more
					sensitive. Optional Value: 1 to 255.
AutoSleepTime			@ 0xF9
		Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1		Bit0
Desc.					AutoSleepTime
		Bit Name			description
		[7: 0] AutoSleepTime			When no touch, into low power mode automatically x seconds.
					Unit 1S, default is 2S.
IrqCtl			@ 0xFA
		Bit7	Bit6	Bit5	Bit4		Bit3		Bit2	Bit1		Bit0
Desc.		EnTest EnTouch EnChange OnceWLP place
		name			description
		[7]	EnTest		Interrupt pin to test, enable automatic periodic issued after a low pulse.
		[6]	EnTouch		When a touch is detected, a periodic pulsed Low.

[5]		EnChange		Upon detecting a touch state changes, pulsed Low.
[4]		EnMotion		When the detected gesture is pulsed Low.
[0]		OnceWLP		Press gesture only issue a pulse signal is low.
AutoReset		@ 0xFB
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2		Bit1		Bit0
Desc.				DebouceTime
	Bit Name			description
	[7: 0] DebounceTime			X seconds but no valid touch gesture, automatically reset. Unit 1S, do
				not enable this function is zero. The default is 5.
LongPressTime		@ 0xFC
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2		Bit1		Bit0
Desc.				LongPressTime
	Bit Name			description
	[7: 0] LongPressTime			Press automatically reset after x seconds.
				Unit 1S, do not enable this function is zero. The default is 10.
IOCtl		@ 0xFD
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2		Bit1		Bit0
Desc.						SOFT_RST IIC_OD				En1v8
	Bit Name			description
[2]		SOFT_RST		Master reset by pulling the soft touch IRQ pin implemented. 0: Disable
				soft reset. 1: Enable soft reset.
[1]		IIC_OD		IIC pin drive mode, the default pull-up resistor. 0: pull-up
				resistor 1: OD
[0]		En1v8		IIC and IRQ pin level selected, the default is the VDD level. 0: VDD 1:
				1.8V
DisAutoSleep		@ 0xFE
	Bit7	Bit6	Bit5	Bit4	Bit3	Bit2		Bit1		Bit0
Desc.				DisAutoSleep
	Bit Name			description
	[7: 0] DisAutoSleep			The default is 0, automatically enabled into low power mode. Is a
				non-zero value, to disable automatic into low power mode.